## Slide 1
PHD THESIS PROJECT · PHD PROGRAM IN TRANSPORTATION SYSTEMS
Sensor-based Recyclables Collection Planning
Collection Planning
Planeamento de Recolha de Resíduos Recicláveis com Informação de Sensores
Esmaeil Keyvanloo Supervisor: Professor João Fonseca Bigotte University of Coimbra · Coimbra, July 28, 2026

## Slide 2
PRESENTATION OUTLINE
What We Will Cover Today
1
WSmartRoute+ Project
2
Background & Rationale
3
Research Gap
4
Research Question & Objectives
5
Case Study: Rio Maior, Portugal
7
Operational Database & Waste Generation Modelling
8
Waste generation Modelling & Regression Analysis
9
Deterministic Facility Location Model
10
WHY STOCHASTIC OPTIMISATION? From Fixed Demand to Robust Strategic Planning
11
CONCLUSION
1
PROPOSED METHODOLOGY
6

## Slide 3
GOAL Develop intelligent and sustainable municipal waste collection systems.
IoT
Sensors
→
Demand
Forecasting
→
Facility
Location
→
Vehicle
Routing
→
Decision
Support
MY PhD FOCUS
Strategic Infrastructure Planning
Waste Demand Modelling | Deterministic Facility Location | Stochastic Facility Location
My research contributes is limited the strategic planning level of the WSmartRoute.
1.WSmartRoute+ Project
FCT Research Project

## Slide 4
WHY IT MATTERS
2. Background & Rationale
Traditional planning (blind collection)
Fixed collection schedules
No demand estimation
ignores fill levels,
Fails to capture spatial and temporal demand variability.
Reality of waste generation
Dynamic and uncertain
Spatially and temporally variable
Requires data-driven demand estimation
Key Takeaway:
.
Static planning is insufficient. Data-driven demand estimation enables robust infrastructure planning.

## Slide 5
From Reactive Waste Collection to Predictive Infrastructure Planning
Research Streams Commonly Studied Separately
+
Proposed integrated framework
This research integrates three sequential components into a unified decision-support framework:
→
Stochastic Facility Location
Waste Generation Modeling
Facility-location planning
Demand uncertainty
+
→
Deterministic Facility Location
Demand Estimation
3.RESEARCH GAP
The Core Research Gap
Fixed collection schedules
Deterministic demand assumption
Reactive ("blind") collection
Current Planning Limitations
Key Takeaway:
Existing studies typically investigate waste demand modelling, facility location, and demand uncertainty as separate research problems. Few study integrate these components into a unified decision-support framework.
This research proposes a sequential decision-support framework that integrates demand estimation with deterministic and stochastic facility-location models to support robust strategic municipal waste infrastructure planning under demand uncertainty

## Slide 6
4. MAIN RESEARCH QUESTION
RESEARCH OBJECTIVES
01
02
03
04
“How can waste generation modelling be integrated with deterministic and stochastic p-median facility location models to improve strategic municipal solid waste container planning under demand uncertainty?”
System Characterisation
Characterise the existing municipal solid waste collection system in Rio Maior and develop the spatial and operational database.
Waste Generation Modelling
Develop and validate statistical models for estimating municipal solid waste generation.
Deterministic Facility Location
Develop a deterministic p-median model to identify baseline strategic container locations.
Stochastic Facility Location
Extend the deterministic model to explicitly incorporate demand uncertainty.
Overall Goal: Develop a robust and transferable framework for strategic municipal waste planning under demand uncertainty

## Slide 7
5. Case Study: Rio Maior, Portugal
Municipal Profile
Area: 272 km², Santarém District, Central Portugal
Population: 21,004 inhabitants (2021Census (
Recycling Infrastructure: different ecoponto container typologies
Company Valorsul responsible all management system
Operational database (2020–2024): GIS layers, sensor records, driver observations and collection data
Operational Challenges
Fixed collection schedules independent of actual fill levels ("blind collection")
Partial sensor coverage with hybrid monitoring (IoT + driver observations)
Seasonal variation from and summer activity
Limited financial and technical resources - representative of medium-sized EU municipalities
Key Takeaway:
These characteristic make Rio Maior a representative real-world case study for developing and validating data-driven methods for strategic municipal waste infrastructure planning.

## Slide 8
6 · PROPOSED METHODOLOGY
A Sequential, Data-Driven Research Framework
1. System Characterisation & Database Development
Input • Historical collection records • GIS layers • Demographic data • Land use data Output Container-level database
2. Waste Generation Modelling
• Stepwise regression
Output Estimated waste generation
3. Deterministic Facility Location
• Deterministic p-median • Determine optimal facility locations
Output Baseline facility location solution
4. Stochastic Facility Location
• Demand uncertainty • Stochastic p-median
Output more Robust strategic facility-location decisions
KEY MESSAGE: From data to robust strategic infrastructure planning under demand uncertainty.
Each stage provides the input for the next, creating an integrated decision-support framework for strategic municipal waste infrastructure planning.

## Slide 9
7.Operational Database
Historical Collection
records
GIS spatial data
Demographics information
Land-use
characteristics
Integrated analytical database
2020–2024 · Bin-event → Bin-day → Bin-level
Stepwise Multiple
Regression
Stepwise variable selection
Candidate Models
Strict / Borderline
/ Best-AIC
Selected candidate models
Waste Generation Modelling
Dependent variable:
Average daily waste per container
Candidate predictors:
Population · Distance to CBD · Land-use proportions
Model evaluation criteria:
R2 ,Adjusted R2
AIC-BIC
VIF(multicollinearity)
Residual diagnostics ( normality , Homoscedasticity)
Initial Full OLS
R² = 0.013
low explanatory power
Model refinement required
Initial specification not adequate
Data Sources
Regression Modeling Workflow

## Slide 10
8.WASTE GENERATION MODELLING
From Full OLS to a Parsimonious Model
Full OLS Model
All candidate explanatory variables
R² = 0.013
→
Stepwise Regression
Systematic variable
selection procedure
→
Alternative Candidate Models
Strict ·
Borderline
Best-AIC
→
Final Selected Model
Strict Stepwise Model
(most parsimonious)
Stepwise Multiple Regression Model
Regression Equation: log(1+Y) = 5.186 + 0.000477 × Population_Buffer + 0.000212 × Distance_to_CBD
R²
0.074
Maximum VIF
1.081 (no multicollinearity)
Breusch-Pagan p
0.323 (No evidence of heteroskedasticity )
Key Findings:
Population within the 100 m buffer was significant.
Distance to the CBD was significant.
Demand Equation: Y = exp(5.186 + 0.000477 × Population_Buffer + 0.000212 × Distance_to_CBD_m) - 1
objective of this model is demand estimation rather than behavioural prediction
Estimated demand for 452 containers.
Average estimated demand = 341.24 kg/day.
Compared using statistical and diagnostic criteria

## Slide 11
✓ Residuals are approximately normally distributed in the central region.
✓ Moderate deviations appear in the tails.
✓ Normality assumption is reasonably satisfied.
✓ Overall, the residual diagnostics support the adequacy of the regression model for estimate waste genaration
✓ Residuals randomly scattered around zero
✓ No systematic pattern detected
✓ Approximately constant variance
✓ Breusch–Pagantest : p = 0.323 (> 0.05)
Conclusion: Homoscedasticity assumption is satisfied.

## Slide 12
9.Deterministic Facility Location Model
Mathematical Formulation
Objective: Minimize total weighted distance
between demand points and selected sites
(facility location)
Constraints: Exactly p facilities open; each demand point assigned once; binary decision variables.
Implementation
Software: FICO Xpress Optimizer, Mosel
Method: Dual simplex
Test Scenario Results
3 Facilities Selected
Sites 1, 6, and 7 from 8 candidates
10
population centers
(Demand Points)
2,770 Residents
Population covered
106.6 m
Average service distance
Key ASSUMPTION
Waste demand is fixed and known throughout the planning horizon
OUTPUT
Baseline facility-location solution
min Σᵢ Σⱼ wᵢ dᵢⱼ Xᵢⱼ
The deterministic model generated a feasible baseline facility-location solution under fixed demand assumptions.
This solution is integrated into the subsequent stochastic optimization model, where demand uncertainty is explicitly incorporated to support more robust strategic facility-location decisions.

## Slide 13
Three optimal ecoponto locations (Sites 1, 6, and 7) were selected.
All population centres are assigned to the nearest selected facility.
The solution minimizes the total demand-weighted travel distance while ensuring full service coverage.
This deterministic solution provides the baseline facility-location configuration for the subsequent stochastic optimisation model.
Assumption: fixed and known waste demand
Deterministic Facility Location Results (FICO Xpress)
The solution minimises the total demand-weighted travel distance while ensuring full service coverage.

## Slide 14
10 · Why Stochastic Facility Location?
From Fixed Demand to Robust Strategic Planning
DETERMINISTIC p-MEDIAN
  • Fixed demand
  • Single demand estimate
  • Static assumptions
  Baseline solution
REAL-WORLD CONDITIONS
  • Seasonal variation
  • Population dynamics
  • Tourism
  • Behavioural variability
Dynamic & uncertain demand
STOCHASTIC APPROACH
  • Explicit uncertainty
  • Robust optimisation
  • More robust facility-location decisions
  • More resilient infrastructure planning
More robust strategic planning
Fixed Demand
≠
Real Municipal waste Generation
KEY MESSAGE: Municipal waste demand is inherently uncertain. therefore, strategic facility-location decisions should explicitly account for uncertainty rather than relying solely on deterministic demand assumptions
Current Approach
Real-World Challenge
Proposed Solution

## Slide 15
11.CONCLUSION
Towards a Unified Framework for Municipal Solid Waste Infrastructure Planning
RESEARCH CONTRIBUTION
This research proposes a sequential, data-driven framework integrating waste demand modelling with deterministic and stochastic facility-location optimisation for strategic municipal recycling infrastructure planning under demand uncertainty.
STEP 1
Waste Demand Modelling
• Demand estimated using stepwise regression
• population with buffer area and CBD distance identified as most significant predictors
• demand estimates used as input for facility location
STEP 2
Deterministic Facility location
• Deterministic p-median developed.
• Generated a baseline facility –location configuration
Provides a reliable baseline strategic solution
Minimize total weighted distance
between demand points and selected sites under fixed demand
STEP 3
Stochastic Facility location
• Explicitly incorporates demand uncertainly (seasonality , population dynamics, behaviour, tourism). • proposes a stochastic optimization framework
objective is supports more robust facility -locations decision and supports more resilient infrastructure planning under real world condition
Thank You for Your Attention
Overall contribution: integration of waste demand estimation, deterministic optimization, and stochastic optimization into a unified decision –support framework for strategic municipal infrastructure planning